## Slide 1: LASER TECHNOLOGY
By
Dr P S Reddy
Department of Physics
NIT Goa

## Slide 2: WHAT IS LASER
?

## Slide 3: Incandescent vs. Laser Light
Many wavelengths
Multidirectional
Incoherent
Monochromatic
Directional
Coherent
Long wave drives
High Intensity

## Slide 4: Interaction of radiation with matter
Absorption
Spontaneous Emission
Stimulated Emission

## Slide 5: Absorption
Energy is absorbed by an atom, the electrons are excited into vacant energy shells.

## Slide 6: Spontaneous Emission
The atom decays from level 2 to level 1 through the emission of a photon with the energy hv. It is a completely random process.

## Slide 7: Stimulated Emission
atoms in an upper energy level can be triggered or stimulated in phase by an incoming photon of a specific energy.

## Slide 8: Two-level Laser System
Unimaginable
as absorption and stimulated processes neutralize one another.
The material becomes transparent.

## Slide 9
Two-, three-, and four-level systems
Two-level system
Laser Transition
Pump Transition
At best, you get equal populations. No lasing.
It took laser physicists a while to realize that four-level systems are best.
Four-level system
Lasing is easy!
Laser Transition
Pump Transition
Fast decay
Fast decay
Three-level system
If you hit it hard, you get lasing.
Laser Transition
Pump Transition
Fast decay

## Slide 10: Three-level Laser System
Initially excited to a short-lived high-energy state .
Then quickly decay to the intermediate metastable level.
Population inversion is created between lower ground state and a higher-energy metastable state.

## Slide 11
Ruby laser

## Slide 12: Four-level Laser System
Laser transition takes place between the third and second excited states.
Rapid depopulation of the lower laser level.

## Slide 13
Nd:YAG laser
He-Ne laser

## Slide 14: Laser Output
Continuous Output (CW)
Pulsed Output (P)
Energy
Time
Energy
Time

## Slide 15: Main components of a laser
Medium
Excitation mechanism
Cavity (or) resonator

## Slide 16: Excitation mechanism

## Slide 17
Resonator
  Confines light within the excitable medium, thus tttassuring stimulated emission

## Slide 18: Lasing Action

## Slide 20: Laser Types
According to the active material:
Gas ,Solid-state, Dye, Semiconductor lasers, Excimer and Doped fiber lasers
According to the wavelength:
infra-red, visible, ultra-violet (UV) or x-ray lasers.

## Slide 21: Gas Lasers
Atomic
Molecular
Ionic

## Slide 22
He-Ne laser

## Slide 23: CO2 gas laser

## Slide 24: Ionic Laser

## Slide 26
Schematic diagram of a dye laser
DYE LASER
A dye laser can be considered to be basically a four-level system.
The energy absorbed by the dye creates a population inversion, moving the
electrons into an excited state.

## Slide 27
Semiconductor lasers
photon production by electron hole pair recombination as in LED
above a treshold current, stimulated emission occurs -> lasing
L =n λ
CD player: GaAs, 5mW, 840 nm
Laser printer: AlGaAs, 50mW, 760 nm
Telecom: GaInAlP, 20 mW, 1300 nm
compact, cheap, variable wavelength

## Slide 28: Energy levels in the Excimer Laser
R:noble gas atom
H:halogen

## Slide 29: Excimer laser Diagram

## Slide 30
Er dopant added to core
Pump at 980nm with laser diode
Erbium-doped fiber amplifier (EDFA)

## Slide 31: Applications
Scientific
Military
Medical
Industrial and commercial
Communication

## Slide 32: Scientific
. Spectroscopy
. Lunar laser ranging
. Photochemistry
. Laser cooling
. Nuclear fusion

## Slide 33: Military
. Death ray
. Defensive applications
. Strategic defense initiative
. Laser sight
. Illuminator
. Rangefinder
. Target designator

## Slide 34: Medical
. eye surgery
. cosmetic surgery

## Slide 35: Laser Resurfacing (CO2) Laser skin resurfacing refers to a skin peeling procedure which uses a specific wavelength of light to selectively eliminate:
Fine lines
Wrinkles,
Acne scars
Unwanted Skin Blemishes
Keloid Scars
Procedure performed by Dr. David Harvey

## Slide 36
“Laser Scalpel”
Increased precision
Microsurgery
Improve operations tttvia endoscopes
Diagnostic imaging
Numerous other tttapplications

## Slide 37: Industry & Commercial
. cutting, welding, marking
. CD player, DVD player
. Laser printers, laser pointers
. Photolithography
. Laser light display

## Slide 38: Communication
Doped fibers for amplification
Laser diodes
Optical connectivity's

## Slide 39
http://demonstrations.wolfram.com/LowerExcitedStatesOfHeliumAtom/